About Team Newbies
Team Details
Students of SRM instute of Science and technology .

---
Problem Statement
For Chennai Airport , design and develop an automated sanitizer dispenser ,detect humanpresence through the sensor and dispence sanitizer of 5ml AT the entrance

---
Design & Hardwares

---
Microcontroller
 Arduino UNO – used
The Arduino Uno is an open-source microcontroller board based on the Microchip ATmega328P microcontroller and developed by Arduino
   Alt - Arduino nano ,ATtiny84, or	Attiny85
Actuator
Sensors
An actuator is a device that uses a form of power to convert a control signal into mechanical motion. ..
</> Pump Motor
</> L298 motor driver Module
 proximity sensors - An infrared (IR) sensor is an electronic device that measures and detects infrared radiation in its surrounding environment.
Indicators
An indicator is a specific, observable and measurable thing that can be used to show changes or progress a programme is making toward achieving a specific output.
<?> buzzers
<?> LED Strips

---
Team Newbies
Tech Specs
Microcontroller & sensor
Power Supply
Actuator & indi...
4 x 3.7 v lithium battry cells , which gives 12 + v dc current
Arduino uno - 5 v,14 D,6 ~pin
IR sensor – 5 v ,4 pin
Attiny84 – 1.8 -5 v , 14 pin
Attiny85 – 8 pin
Pump Motor – 12v , 2pins
L298 – 12v or 5v , 10 pins
Buzzer – 5v ,2pins
LED strip – 12v ,2 pins

---
Team Newbies
        Motor function is called to turn the acutuators (MOTOR , LED and the buzzer) ON , after 500 ms the motor will be turned OFF , hence the dispensing effect is created and the motor should get the sanitizer to the valve
        But the led and the buzzer is reamin ON till the checkexit function ends . Here check exit function is used to prevent sanitizing the same hand again
        Then the led and buzzer will be OFF , and the prototype will be ready in a loop for the next trigger
        Also we include one more function called hummaneffect to blynk the led and buzzer ., to indicate that the human need to take the hand back .
Advantages &
Working
When the the prototype is turned ON , first the arduino uno will read the input signal fromthe pin 3 . were IR sensor’ Out pin is connected .
  Next , As per the program conditional loop will occure . If the the IR sensor module sence the human presence . It will call the MotorON function and Checkexit function . Were the two functions are user defiend function

---
Team Newbies
what if the person still keeps his hand and doesn't take it off for a few second
since we were all separated coz of covid situation so we could only discuss the project through google meet
one of the problems we faced was the lack of proper pieces of equipment
Flow of water due to internal pressure nd gravity

---
Cost Analysis
        Arduino uno – 400
Led strips - 60
L298 – 100
      Lithium cells – 80
Wires – 20
   Ir sensor – 120
 Buzzer - 50

---
THANK YOU
Yellow Idea Template for LibreOffice Impress.
Credit by : @ealita.id, 2020.